Second LACCEI International Latin American and Caribbean Conference for Engineering and Technology (LACCEI’2004)

“Challenges and Opportunities for Engineering Education, Research and Development”

2-4 June 2004, Miami, Florida, USA

##### Sizing of Deep Subaqueous Pits for Dredged Material Disposal

Paul R. Schroeder, Ph.D., P.E.

Research Civil Engineer, US Army Engineer R&D Center, Vicksburg, MS, USA

Stephen A. Pranger

Chemical Engineer, US Army Engineer R&D Center, Vicksburg, MS, USA

Thomas D. Borrowman

Research Civil Engineer, US Army Engineer R&D Center, Vicksburg, MS, USA

Guilherme R. Lotufo, Ph.D.

Research Biologist, US Army Engineer R&D Center, Vicksburg, MS, USA

Abstract

Dredging of the navigational channel of the Piaçaguera Canal is required to maintain access to its principal harbor, which is situated in the inner Santos estuary of Brazil and is an area of intense sedimentation.  Biological and chemical testing of sediment from the berthing area clearly indicates that a portion of these sediments will require confined disposal when dredged.  The available sites in the Santos region for placement of unsuitable material are limited; therefore, confined aquatic disposal in excavated pits in the channel is being examined.  Sizing of pits considering hydraulic placement is critical due to the small width of the channel, capping requirements, and constraints on side slopes restricting excavation depth.  Therefore, accurate prediction of storage requirements is critical.  Precise characterization of the physical, geotechnical, settling and consolidation properties is required for modeling sedimentation/ consolidation.  Standard compression settling, self-weight and standard oedometer consolidation tests were run.  Standard compression settling tests and self-weight consolidation tests often predict significantly different storage requirements due to difficulties in acquiring precise, accurate permeability data.  Therefore, a 5-m (incrementally loaded for 40 days) compression settling test was run to simulate the disposal process and verify the self-weight consolidation predictions.

Keywords

Dredging, CAD, Capping, Sizing, Consolidation

1. Introduction

The main harbor in Cubatão (State of São Paulo, Brazil) and its navigation channel are located in the inner area of the Santos estuary, an area of high sedimentation.  The estuary is situated down the slopes of a mountain chain where intense rainfall and high energy river systems erode large amounts of soils and sediments to deposit in areas of the estuary.  It was estimated that an area of 260 km2 drains into the Piaçaguera Canal and that its average sediment deposition rate is 35,000 m3/month or 400,000 m3/year.

The harbor and access channel need dredging, as disruption of navigation is eminent.  The channel is 5.4 km long and 100 m wide.  The estimated amount of sediment to be dredged is 3.5 million m3, 25% of which is in the harbor itself.  The target depth of the channel is 13 m.  The dredging depth is 2-3 m on average for the channel and a little higher for the harbor area.

Biological and chemical testing of the sediments clearly indicates that sediments from the berthing area and upper reaches of the channel will require confined disposal when dredged.  The available sites in the Santos region for placement of unsuitable material are limited; therefore, confined aquatic disposal in excavated pits in the channel is being examined.  Sizing of pits considering hydraulic placement is critical due to the small width of the channel, capping requirements, and constraints on side slopes restricting excavation depth.  Therefore, accurate prediction of storage requirements is essential.

Figure 1:  Piaçaguera Canal, Harbor         	             Figure 2:  Sites of Contaminated Sediments

and Navigation Channel 			                 (shown as darker areas)

1.1 Objective

The project objective was to generate the best estimate of storage requirements for use in sizing the CAD cells for the proposed hydraulic dredgng project and to reduce the uncertainty of the prediction by using three methods of analysis.

1.2 Scope of Work

The scope of work consisted of physical/geotechnical characterization of the sediments, laboratory settling and consolidation testing, and prediction of dredged material storage requirements based on settling and consolidation analysis.  Self-weight and standard oedometer consolidation tests were run.  Standard compression settling tests were run on dredged material and capping materials.  A 5-m tall, incrementally loaded compression settling test was also run to more accurately simulate the actual filling of a CAD cell by hydraulic pumpout from a hopper dredge.

2. Methodologies

2.1 Dredged Material Characterization

Physical/geotechnical characterization of the sediments consisted of measuring the following parameters in accordance with the USACE Soil Testing Guidelines (USACE 1970): grain-size distribution, liquid limit, moisture content, specific gravity, self-weight and standard oedometer consolidation and compression settling.  Compression settling tests were conducted in accordance with the Engineer Manual 1110-2-5027 entitled Confined Disposal of Dredged Material (USACE 1987).

2.2 Capacity Requirements

The bottom layers of settled material will exhibit compression settling or thickening.  As settled solids accumulate, the concentration of settled solids in the bottom layers increases.  Successive layers of settled solids then rest on each other.  The point at which the bottom layer begins to provide some physical support, compression settling begins.  The change from flocculent or zone settling to compression settling occurs at a concentration of approximately 200 to 300 g/L for most dredged material slurries.

Storage requirements for the material to be hydraulically placed were predicted using the USACE ADDAMS (Schroeder and Palermo 2004) SETTLE module for compression settling and the ADDAMS PSDDF module for consolidation.

SETTLE uses compression settling test data to determine the average concentration of settled solids within the confined disposal facility (CDF) at the end of disposal.  This design concentration is used to calculate the initial storage requirements for the fine-grained (smaller than No. 200 sieve) fraction of the dredged material.  Coarse-grained (larger than No. 200 sieve) material behaves independently, and its storage volume is determined based on its mass.  The storage volumes of the two fractions are summed to yield the minimum initial storage required.  The volume is an estimate of the short-term storage requirements for the single disposal project under consideration.

SETTLE implements CDF design procedures described in Engineer Manual 1110-2-5027 (USACE 1987) and subsequent guidance documents.  It performs CDF design calculations based on analysis of laboratory settling test data, information on the dredging project, anticipated dredged volumes, and dredged material characteristics.

From the interface height of the settled solids and initial solids concentration data, SETTLE computes the average settled solids concentration at each time the interface height was measured.  The settled solids concentration versus time data are fitted (using the least squares technique) to a power curve of the form:

where  C   =  average concentration of settled solids, g/L; T   =  time since disposal, days; and a,b  =  regression coefficients.

The one-dimensional Primary consolidation, Secondary compression, and Desiccation of Dredged Fill (PSDDF) model utilizes finite strain consolidation theory to estimate changes in dredged material surface elevation with time.  The model solution is well suited for the prediction of consolidation in thick deposits of very soft, fine-grained soils, such as dredged material, because it provides for the effects of (a) self-weight consolidation, (b) permeability varying with void ratio, (c) a non-linear void ratio-effective stress relationship, and (d) large strains.  The model allows determination of the optimal filling schedule and quantification of the effects of operational techniques on the service life of confined dredged material placement areas.  In addition, the time rate of settlement for dredged material placed underwater for disposal or land creation purposes is also of interest.  Settlement of submerged dredged material is subjected to the effects of (a) self-weight consolidation, (b) surcharge induced consolidation usually by placement of a cohesionless soil cover, and (c) secondary compression.  The program can also simulate underwater placement of cohesive or cohesionless soils.  The major input required by PSDDF is the void ratio-effective stress and void ratio-permeability relationships obtained from laboratory consolidation tests on the dredged fill and compressible foundation materials.

3. Results

3.1 Compression Settling

Compression settling tests were run in a 2-m tall, 20-cm diameter column on slurries of dredged material at 120 g/L and capping material at 119 g/L.  The capping material consists of fine-grained sediments from the less contaminated, lower reaches of the navigational channel and has very similar physical/ geotechnical properties to the dredged material.  The results of the compression settling tests are shown in Figure 3.  Assuming a disposal period of 60 days (mean residence of 30 days), the dredged material would be expected to achieve a concentration of 314 g/L while capping material would reach 318 g/L.

Figure 3:  Standard Compression Settling Results

3.2 Primary Consolidation

Both self-weight and standard oedometer consolidation tests were run on the dredged material.  The test data were reduced assuming large strain, singly drained consolidation theory to estimate the permeability of the material.  Results of the tests were integrated together to develop smooth relationships of void ratio versus effective stress and void ratio versus permeability for the expected range of void ratios.  The consolidation properties are given in Figures 4 and 5.

Figure 4:  Void Ratio – Effective Stress Relationships

Figure 5:  Void Ratio – Permeability Relationships

The PSDDF consolidation model was run to model the hydraulic filling of a CAD cell over a 60-day period to an average depth of storage of 4 meters, assuming an impermeable bottom.  The model predicted an average settled solids concentration of 394 g/L.

3.3 Tall Column Compression Settling

Due to the large thickness of the proposed deposit relative to the standard lift used in the compression settling test and the difficulty in acquiring accurate permeability data in the consolidation test, a tall column compression settling test was run to better simulate the proposed disposal.  The column was incrementally loaded with a 0.3-m lift of sediment slurry for each of 38 days.  The resulting concentrations of settled solids are shown in Figure 6.  Assuming a disposal period of 60 days, the dredged material would be expected to achieve a concentration of 353 g/L.

Figure 6:  Tall Column Compression Settling Results

4. Conclusions and Recommendations

The results for the tall column compression settling test provide the best basis for sizing the CAD cells.  The results are somewhat higher than the standard compression settling results as would be expected due to the greater effective stresses in the test resulting from using an effective thickness that was about 5 times greater.  Decreasing the permeability data in the consolidation modeling by 50 percent would have yielded similar results, which is within the range of errors in estimating permeability.

5. Acknowledgments

We are grateful to acknowledge the Companhia Siderúrgica Paulista (COSIPA) and the Fundação de Estudos e Pesquisas Aquáticas (FUNDESPA) for supporting this study.

6. References

Schroeder, P. R. and Palermo, M. R.  (2004).  "The Automated Dredging and Disposal Alternatives Management System (ADDAMS)," Environmental Effects of Dredging Technical Notes EEDP-06-12, U.S. Army Engineer Waterways Experiment Station, Vicksburg, MS.

USACE (1970). "Laboratory Soils Testing," Engineer Manual EM 1110-2-1906, Washington, DC.

USACE (1987). "Confined Disposal of Dredged Material," Engineer Manual EM 1110-2-5027, Washington, DC.

# Text boxes

## Figure 1. Dimensions of final proceedings page

Times New Roman Font, Size 8 pt, Italic, Single spacing, Left Justify

(This text must be typed by the authors and should appear on the first page only)

Times New Roman Font, Size 11 pt, Bold, Single spacing, Center

Figures must centralized

Times New Roman Font, Size 11 pt, Single spacing, Center

Times New Roman Font, Size 10 pt, Bold, Single , spacing, Center

Figures must be placed in the center of the page

21 cm

29.7 cm

3 cm top margin

Side and bottom margins

2.5 cm each